## Slide 1: PUMPING
Do not pump the rifle more than once per shot.
If the air rifle is pumped more than once, or left with full chamber pressure for an extended period, the compressed air may not expel completely upon firing
A cadet coach may assist the shooter in pumping the rifle
Level One 421.04a
OHP # 1

## Slide 2: LOADING
Pick up and hold the rifle with your left hand.
Ensure the safety catch is in the ON (no red) position.
In accordance with safety precautions, rifle should already
be in safe status with bolt open fully to the rear and pump
lever left partially open.
Pump the rifle.
When the pump lever is fully extended, pause about three
seconds.
Load the pellet or 5-shot pellet clip (the flat end faces forward).
Close the bolt.
Level One 421.04a
OHP # 2

## Slide 3: FIRING
Place the safety, catch in the OFF (red) position.
Aim rifle at the target.
Squeeze the trigger.
Open the bolt.
Repeat sequence for each shot.
Place the safety catch in the ON (no red) position and
partially open the pump lever immediately after firing
the practice.
Lay down the rifle.
Level One 421.04a
OHP # 3

## Slide 4: UNLOADING
Pick up the rifle
Remove 5-shot pellet clip.
Pump the rifle.
Close bolt.
Place the safety catch in the OFF
(red) position.
Aim rifle at target.
Level One 421.04a
OHP # 4

## Slide 5: UNLOADING
Fire the action.
Open the bolt.
Place safety catch in the ON (no red) position.
Open the pump lever 5-8 cm (2-3 inches).
Wait to be cleared by range staff.
Lay down the rifle.
Remove eve and ear Protection.
Level One 421.04a
OHP # 5

## Slide 6: Place a number in the blank provided to show the correct order for the specified procedure.
LOADING
When the pump lever is fully extended, pause about three seconds.
Close the bolt.
Pump the rifle.
Pick up and hold the rifle with your left hand.
Load the pellet or 5-shot pellet clip (the flat end faces forward).
Ensure the safety catch is in the ON (no red) position. In accordance with safety precautions, rifle should already be in safe status with bolt open fully to the rear and pump lever left partially open.
FIRING
Place the safety catch in the ON (no red) position and partially open the pump lever immediately after firing the practice.
Open the bolt.
Squeeze the trigger.
Aim rifle at the target.
Lay down the rifle.
Place the safety, catch in the OFF (red) position.
Repeat sequence for each shot.
OHP # 6
Level One 421.04a
NAME:

## Slide 7: Place a number in the blank provided to show the correct order for the specified procedure.
Place the safety catch in the OFF (red) position.
Open the pump lever 5-8 cm (2-3 inches).
Lay down the rifle.
Close bolt.
Pick up the rifle
Remove eve and ear Protection.
Fire the action.
Open the bolt.
Place safety catch in the ON (no red) position.
Remove 5-shot pellet clip.
Wait to be cleared by range staff.
Pump the rifle.
Aim rifle at target.
Level One 421.04a
UNLOADING
ANSWER KEY

## Slide 8: Place a number in the blank provided to show the correct order for the specified procedure.
LOADING
When the pump lever is fully extended, pause about three seconds.
Close the bolt.
Pump the rifle.
Pick up and hold the rifle with your left hand.
Load the pellet or 5-shot pellet clip (the flat end faces forward).
Ensure the safety catch is in the ON (no red) position. In accordance with safety precautions, rifle should already be in safe status with bolt open fully to the rear and pump lever left partially open.
FIRING
Place the safety catch in the ON (no red) position and partially open the pump lever immediately after firing the practice.
Open the bolt.
Squeeze the trigger.
Aim rifle at the target.
Lay down the rifle.
Place the safety, catch in the OFF (red) position.
Repeat sequence for each shot.
OHP # 7
Level One 421.04a
NAME:
1
2
3
4
5
6
1
2
3
4
5
6
7

## Slide 9: Place a number in the blank provided to show the correct order for the specified procedure.
Place the safety catch in the OFF (red) position.
Open the pump lever 5-8 cm (2-3 inches).
Lay down the rifle.
Close bolt.
Pick up the rifle
Remove eve and ear Protection.
Fire the action.
Open the bolt.
Place safety catch in the ON (no red) position.
Remove 5-shot pellet clip.
Wait to be cleared by range staff.
Pump the rifle.
Aim rifle at target.
ANSWER KEY
Level One 421.04a
UNLOADING
1
2
3
4
5
6
7
8
9
10
11
12
13