## Slide 1: Navigating Position
Position is determined by a grid system of intersecting circles on the earth’s surface.
Those running north and south are Meridians of Longitude.
Those running east and west are Parallels of Longitude.
Level Three 417.04A
OHP # 1

## Slide 2: Calculating Coordinates
There are two lines from which coordinates are calculated.
The Equator, a great circle on the surface of the earth lying equidistant from the poles.
The Prime Meridian, which is the meridian passing through Greenwich, England.
Level Three 417.04A
OHP # 2

## Slide 3: Longitude
There 360 meridians of longitude which all converge a the true north and south poles.
Longitude is measured from 0-180 degrees east and west of the Prime Meridian.
The Prime Meridian is numbered 0 degrees.
The 180th meridian is called the International Date Line.
Longitude is measured in degrees, minutes and seconds. 60’=1º & 60’’=1’
Level Three 417.04A
OHP # 3

## Slide 4: Longitude
Level Three 417.04A
OHP # 4

## Slide 5: Latitude
There are 180 parallels of latitude.
Latitude is measured from 0 to 90 degrees north or south of the equator.
The Equator is numbered 0 degrees.
Latitude is also expressed in degrees, minutes and seconds.
Lines of latitude are parallel and are thus referred to as parallels. Parallels of latitude do not converge.
Level Three 417.04A
OHP # 5

## Slide 6: Latitude
Level Three 417.04A
OHP # 6

## Slide 7: Position by Coordinates
The position of anywhere on earth can be expressed as the intersection of a parallel of latitude and a meridian of longitude.
When this is done, the latitude is written first, followed by the longitude coordinate.
Ex: Winnipeg is 49º 54’N 97º 14’W
Level Three 417.04A
OHP # 7